## Slide 1: 2015 Residential Energy Consumption Survey (RECS)
Webinar
September 19, 2017 at 2 p.m. EDT
By
Chip Berry, Survey Manager
Danni Mayclin, Survey Statistician
Maggie Woodward, Industry Economist

## Slide 2: Agenda
Introduction
  RECS release schedule
  Accessing RECS data on the website
Highlights from the 2015 RECS
Overview of methods for the 2015 RECS
A look to the future
Q&A

## Slide 3: 2015 RECS release schedule
Product | Release date
Housing characteristics data tables | February 2017
Microdata and methodology | May 2017
Square footage data | Fall 2017
Energy consumption and expenditures data | Spring 2018

## Slide 4: The RECS website
www.eia.gov/consumption/residential/

## Slide 5: Highlights from the 2015 RECS

## Slide 6: RECS results describe the characteristics that contribute to energy consumption in homes
More than 240 items collected
  Structure and geography
  Appliances and electronics
  HVAC and water heating
  Lighting
  Program participation
New questions for 2015
  Smart meters and smart thermostats
  LED lighting
  Thermostat use
Highlights variability across homes

## Slide 7: Newer homes are more likely to have high ceilings and more efficient windows
Chart: 
| Before 1960 | 1960 to 1979 | 1980 to 1999 | 2000 to 2015
High ceilings | 0.25833 | 0.19358 | 0.461 | 0.54576
Double or triple pane windows | 0.52698 | 0.54348 | 0.48845 | 0.71181
Notes: Highlight new versus old homes; newer homes also more likely to be in warmer climates

## Slide 8: The number of households with a second refrigerator continues to increase
Chart: 
| 1978 | 1980 | 1982 | 1984 | 1987 | 1990 | 1993 | 1997 | 2001 | 2005 | 2009 | 2015
Two or More | 0.14 | 0.14 | 0.13 | 0.13 | 0.12 | 0.14 | 0.15 | 0.15 | 0.15 | 0.17 | 0.22 | 0.23 | 0.29949

## Slide 9: Dishwashers are the most frequently unused appliance
Chart: 
| Dishwasher | Clothes Washer | Clothes Dryer | Microwave | Stove
Have and use the appliance | 0.54315 | 0.81557 | 0.78849 | 0.94755 | 0.88579
Have but do not use the appliance | 0.13452 | 0.010152 | 0.017766 | 0.013536 | 0.028765
Do not have the appliance | 0.32234 | 0.17428 | 0.19374 | 0.038917 | 0.085448
Notes: Not only captured “have, but don’t use” but also more changed usage questions from categorical to more detailed, continuous response.

## Slide 10: Larger share of households report not using a television
Chart: 
| 1997 | 2001 | 2005 | 2009 | 2015
No TV | 0.013 | 0.01215 | 0.012601 | 0.013204 | 0.026227
1 or 2 TVs | 0.692 | 0.63271 | 0.55806 | 0.54313 | 0.5846
3 or more TVs | 0.295 | 0.35514 | 0.42934 | 0.44454 | 0.38917

## Slide 11: Choice of heating equipment varies within and across climates
Chart: 
| marine | mixed-dry / hot-dry | hot-humid | mixed-humid | cold / very cold | United States
portable electric heater | 1314876 | 1358587 | 2980512 | 6584909 | 7905919 | 20144803
natural gas fireplace | 278557 | 777722 | 631988 | 2026125 | 2812806 | 6527198
wood fireplace | 412577 | 578378 | 1436533 | 1598807 | 1450694 | 5476989
wood stove | 374156 | 112113 | 97031 | 1279721 | 1883066 | 3746087
other equipment | 659908 | 169653 | 663152 | 2323787 | 3571253 | 7387753
none | 3571961 | 9855985 | 16957328 | 19802896 | 24737251 | 74925421
Chart: 
| marine | mixed-dry / hot-dry | hot-humid | mixed-humid | cold / very cold | United States
natural gas furnace | 2656375 | 5665765 | 4520806 | 10363642 | 21837212 | 45043800
natural gas other | 553073 | 1335225 | 714066 | 4056901 | 4227079 | 10886344
electric other | 1143954 | 996709 | 3235616 | 3591359 | 3933678 | 12901316
electric heat pump | 702519 | 894292 | 4215247 | 5065534 | 1258184 | 12135776
electric furnace | 561836 | 1681793 | 7249919 | 5387624 | 3027889 | 17909061
other | 605492 | 293723 | 572402 | 5119152 | 8063593 | 14654362
none | 388786 | 1984929 | 2258488 | 32034 | 13352 | 4677589

## Slide 12: “Set it and forget it” is most common method for controlling central AC systems
Chart: 
| Window/wall air conditioning | Central air conditioning
Set at one temperature | 0.30567 | 0.44592
Manually adjust | 0.18332 | 0.25839
Program thermostat | 0.050516 | 0.18029
Turn on/off as needed | 0.45384 | 0.1149

## Slide 13: Most households have a mix of lightbulbs installed
All
10%
1%
11%
Some
71%
72%
27%
None
18%
19%
71%
Incandescent
CFL
LED

## Slide 14: The proportion of all-electric homes is rising, primarily in the South Census region
Chart: 
| 1993 | 2005 | 2015 | 1993 | 2005 | 2015 | 1993 | 2005 | 2015 | 1993 | 2005 | 2015 | 1993 | 2005 | 2015
Electricity only | 0.16015 | 0.20248 | 0.24888 | 0.064029 | 0.054992 | 0.073581 | 0.076508 | 0.085244 | 0.13426 | 0.15639 | 0.13822 | 0.17423 | 0.27613 | 0.38896 | 0.44407
Electricity and one other fuel | 0.61327 | 0.64563 | 0.65551 | 0.60568 | 0.72267 | 0.73976 | 0.72712 | 0.74803 | 0.76729 | 0.59621 | 0.69159 | 0.72925 | 0.54886 | 0.51497 | 0.50557
Electricity and two or more other fuels | 0.22658 | 0.15189 | 0.095614 | 0.33029 | 0.22234 | 0.18666 | 0.19637 | 0.16672 | 0.098448 | 0.2474 | 0.17019 | 0.096523 | 0.17409 | 0.095526 | 0.050357

## Slide 15: Methods from the 2015 RECS

## Slide 16: RECS Methodology: Overview
Sampling
Questionnaire Design
Data Collection Modes (in-person, web, mail)
Response Rate and Data Quality
Processing and Editing
Imputation and Weighting

## Slide 17: RECS Methodology: Sampling
Addresses were selected to represent the 118.2 million occupied, primary residences in the 50 States + DC
Multi-stage sample designed to produce national, Census Region, and Census Division estimates
First stage: Public Use Microdata Areas (200)
Second stage: Census Block Groups (800)
Final stage: Housing units (12,753)
2. Select CBGs
1. Select PUMAs
Main St
Diagonal Ave
3. Select housing units

## Slide 18: RECS Methodology: Questionnaire Design
Questionnaire design process included:
  Reviewing content from 2009 RECS
  Adding and dropping questions based on current household technologies
  Soliciting data user input
  Pretesting most of the new or substantially revised questions
Households completed RECS questionnaire by one of three methods:
  In-person by computer-assisted personal interview (used since 1997 RECS)
  Self-administered web questionnaire (new!)
  Self-administered mail questionnaire (new!)

## Slide 19: RECS Methodology: Questionnaire Sections
Housing unit characteristics
Appliances
Electronics
Space heating
Air conditioning
Water heating
Lighting
Energy programs
Energy bills
Energy suppliers
Household characteristics
Energy assistance
In-person only: Housing unit measurement
In-person only: Scanning of sample energy bills

## Slide 20: Example: In-person interview vs. Mail
DISHWASH (Changed from 2009) | 
ASK | All respondents
Does your household have a dishwasher? 1 Yes 0 No | 
NEXT | If DISHWASH=1: DWASHUSE Else: IVCOMMBFILTER

## Slide 21: Example: Web screenshot

## Slide 22
2014
2015
2016
2017
Cities Pilot
Energy Supplier Survey
Web and mail pilots
National Pilot
In-person interviews
Web/ paper
2015 RECS
UMD Pilot
RECS Methodology: Data Collection Schedule

## Slide 23: RECS Methodology: Response Rate and Data Quality
2015 RECS response rate was 51%, much lower than 79% for 2009 RECS
  43% of those were in-person, 37% web, 20% mail
Data quality analysis included:
  Comparing to previous RECS and external sources (i.e. American Community Survey conducted by the U.S. Census Bureau)
  Comparing participation by subgroups within the sample
  Looking for non-response bias
  Comparing responses across mode
We found very few significant differences, and most were not practically different

## Slide 24: RECS Methodology: Processing and Editing
Mail questionnaires were keyed twice
Validation to ensure the correct household was interviewed
Post-collection checks included reading comments and reviewing outliers, inconsistent values, and write-in responses
Data from all modes were combined into one file
Added auxiliary weather and geographic variables for each household

## Slide 25: RECS Methodology: Imputation and Weighting
Item imputation was used to fill in missing values in the data set
  216 variables were imputed
  Average imputation rate: 3.7%
Hot-deck imputation method was used – a recipient household was matched with a similar donor household and borrowed its value
Weights are calculated for each responding housing unit
  Sum of all weights is 118.2 million, which is the total number of U.S. households in 2015
If using the public microdata file, please use NWEIGHT variable (see documentation, or ask us how to do this if you aren’t sure)

## Slide 26: The Future of RECS

## Slide 27: Using on-line and paper questionnaires allows for a more flexible RECS program in the future
Opportunities for…
Large samples to cover more detailed geographies and special populations
More frequent data collections
Revisiting sampled households over time for longitudinal analysis
Expert assessments and end-use measurement via submetering devices
Planning about to begin for the next RECS…2020?

## Slide 28: Questions? (Please submit them through the Chat box)

## Slide 29: Contact us!
www.eia.gov/consumption/residential/
Chip Berry, Survey Manager
  James.Berry@eia.gov
Danni Mayclin, Survey Statistician
  Danielle.Mayclin@eia.gov
Maggie Woodward, Industry Economist
  Maggie.Woodward@eia.gov