## Slide 1: Issues in Focus Analysis from International Energy Outlook 2020: Off-Grid Electricity Development in Africa: Uncertainties and Potential Implications for Electric Power Markets
Center for Strategic and International Studies
October 14, 2020 | Washington, DC
Thaddeus J. Huetteman, Team Lead, Electricity Analysis
U.S. Energy Information Administration

## Slide 2: Challenges in the International Energy Outlook 2019 (IEO2019) from a continent-wide, centralized-grid viewpoint of Africa
Africa generation projection includes major growth and contains uncertainty
  Expanding urbanization, but large rural population without electricity access
  Lower pace of transmission development and grid integration
  New opportunities associated with off-grid generation
Uncertainties masked by single region, centralized grid-only view of Africa
  Results in over-optimized projected generation mix in which hydro and solar dominate
Chart: Single Region Africa
| 2019 | 2030 | 2050
coal | 265.3635 | 293.9612 | 150.8454
oil | 78.0129 | 31.0614 | 6.6962
natural gas | 292.3546 | 289.1326 | 391.0214
nuclear | 12.9326 | 22.3886 | 37.8243
hydro | 116.7947 | 199.5813 | 577.2646
wind | 17.8106 | 87.4858 | 101.698
solar | 15.0937 | 94.0849 | 558.3382
other renewables | 5.5104 | 39.8354 | 72.3805
other renewables
solar
wind
hydro
nuclear
natural gas
oil
coal
Source: U.S. Energy Information Administration, International Energy Outlook 2020

## Slide 3: IEO2020 regional differences include greater electricity demand growth potential in the Africa South region
Africa North
  Greater electricity access
  More mature electric sector infrastructure
  Significant reliance on natural gas
Africa South
  Lower electricity access
  Higher potential for electricity demand growth and investment
  Significant reliance on coal/hydro, with new offshore gas reserves discovered in Mozambique and Tanzania
Full electric access by 2030, met by:
  Maximum Grid Expansion
  Maximum Off-grid Expansion
Source : The World Bank: World Bank Electricity Transmission and Distribution data set, 2017

## Slide 4: IEO2020 highlights regional differences in generation mix growth
Highlights transmission limits between regions
Differing role of natural gas in Africa North and coal in Africa South
Natural resources availability influences generation fuel-mix
Expanding investment in LNG facilities for both import/export
Chart: 
| 2019 | 2030 | 2050 | 2019 | 2030 | 2050 | 2019 | 2030 | 2050 | AFR+ | AFR+ | AFR+ | AFR_N | AFR_N | AFR_N | AFR_S | AFR_S | AFR_S
coal | 253.3436 | 245.7156 | 373.8272 | 16.2076 | 11.5716 | 27.8969 | 237.136 | 234.144 | 345.9303
oil | 76.9509 | 28.6432 | 6.6849 | 43.5169 | 16.4601 | 3.7704 | 33.434 | 12.1831 | 2.9145
natural gas | 307.5302 | 391.438 | 689.3403 | 250.3966 | 339.0879 | 544.4462 | 57.1336 | 52.3502 | 144.8941
nuclear | 12.9326 | 22.3886 | 37.8243 | #N/A | #N/A | #N/A | 12.9326 | 22.3886 | 37.8243
hydro | 112.5028 | 160.4983 | 333.972 | 20.4036 | 21.7934 | 21.7934 | 92.0991 | 138.7049 | 312.1785
wind | 17.5321 | 87.7116 | 102.6049 | 10.8645 | 36.6273 | 47.3105 | 6.6676 | 51.0843 | 55.2944
solar | 14.6294 | 78.671 | 246.0823 | 8.669 | 45.5185 | 201.8169 | 5.9604 | 33.1526 | 44.2655
other renewables | 4.7801 | 41.1745 | 75.7116 | 0 | 0.46006 | 0.50035 | 4.7801 | 40.7145 | 75.2113
divider | 5000 | 5000

## Slide 5: IEO2020 calculates bounds for off-grid generation in Africa South and potential for significant expansion of renewables
Assumes Africa South reaches full electricity access by 2030 with incremental demand by sector:
  Residential: unserved urban and rural areas achieve full electricity access by 2030 at average electricity consumption levels
  Commercial/Industrial: replacement of lost load for commercial and industrial customers attributed to Africa’s less reliable power supply and delivery systems
Maximum Grid Expansion case assumes full incremental demand is met by least cost dispatch of centralized-grid power
Maximum Off-Grid Expansion case assigns incremental demand to be met by off-grid supply either in mini-grid or stand-alone solar photovoltaic systems

## Slide 6: Africa South Maximum Grid Expansion maintains growth in fossil fuel generation versus solar growth in Maximum Off-Grid case
Africa South electricity generation by fuel source in Comparative Reference (Two-Region) case (CRC)
Change in Africa South generation from CRC by fuel source: Maximum Grid Expansion/ Maximum Off-grid cases
Chart: 
| 2030 | 2050 | 2030 | 2050
coal | 66.2851 | 106.2919
natural gas | 70.5863 | 57.4729
hydro | 2.9847 | 2.132
wind | 0.47025 | 5.8454
solar | 0.29112 | 46.2617
off-grid | #N/A | #N/A | 141.1458 | 217.8242
divider | 1000
Chart: 
| 2019 | 2030 | 2050
coal | 237.136 | 234.144 | 345.9303
oil | 33.434 | 12.1831 | 2.9145
natural gas | 57.1336 | 52.3502 | 144.8941
nuclear | 12.9326 | 22.3886 | 37.8243
hydro | 92.0991 | 138.7049 | 312.1785
wind | 6.6676 | 51.0843 | 55.2944
solar | 5.9604 | 33.1526 | 44.2655
other renewables | 4.7801 | 40.7145 | 75.2113
solar, off-grid
solar
wind
hydro
natural gas
coal

## Slide 7: IEO2020 projects opportunities for growth in renewables and fossil generation in Africa North and South
Chart: 
| 2019 | 2030 | 2050
coal | 253.3436 | 245.7156 | 373.8272
oil | 76.9509 | 28.6432 | 6.6849
natural gas | 307.5302 | 391.438 | 689.3403
nuclear | 12.9326 | 22.3886 | 37.8243
hydro | 112.5028 | 160.4983 | 333.972
wind | 17.5321 | 87.7116 | 102.6049
solar | 14.6294 | 78.671 | 246.0823
other renewables | 4.7801 | 41.1745 | 75.7116
coal | 310.7688 | 484.7903
oil | 28.6389 | 6.6843
natural gas | 446.1804 | 733.754
nuclear | 22.3852 | 37.8185
other renewables
solar,off grid
solar
wind
hydro
nuclear
natural gas
oil
coal

## Slide 8: Conclusion: Off-grid development could increase solar generation, but bypass of centralized grid is unlikely
Lack of interconnection and slow transmission infrastructure development reinforces reliance on regional fuels
Greater off-grid development boosts solar share
Limited interregional transmission and grid cost-competitiveness at higher demand levels make bypass of the grid less likely
Demand growth for fossil fuels in Africa projected to increase demand for imports, including LNG