## Slide 1: Outlook for North American Natural Gas
For
LDC Natural Gas Forum
November 11, 2014 | Toronto, Ontario, Canada
By
Adam Sieminski, Administrator
U.S. Energy Information Administration

## Slide 2: The Americas are the second largest region in natural gas reserves and resources
regional natural gas reserves and resources, 2012
trillion cubic feet
Source: U.S. Energy Information Administration, Oil and Gas Journal, U.S. Geological Survey, EIA/ARI World Shale Gas and Shale Oil Resource Assessment
Chart: 
| Middle East and North Africa | Americas | Former Soviet Union | Asia and Pacific | Sub-Saharan Africa | Europe | South Asia
Proved Reserves | 3117 | 688 | 2178 | 418 | 222 | 145 | 86
Estimated Reservoired Accumulations of Undiscovered Technically Recoverable Gas Resources | 1651 | 1252 | 2145 | 858 | 831 | 184 | 183
Estimated Technically Recoverable Shale Gas Resource | 1003 | 3212 | 415 | 1607 | 390 | 470 | 201

## Slide 3: The Americas hold an abundance of shale gas resources, undeveloped except in the U.S. and Canada
Americas natural gas reserves and resources, 2012
trillion cubic feet
Source: U.S. Energy Information Administration, Oil and Gas Journal, U.S. Geological Survey, EIA/ARI World Shale Gas and Shale Oil Resource Assessment.
Chart: 
| United States | Argentina | Canada | Brazil | Mexico | Venezuela | Colombia | Bolivia
Proved natural gas reserves | 334 | 13 | 67 | 14 | 17 | 196 | 7 | 10
Estimated reservoired accumulations of undiscovered technically recoverable gas resources | 412 | 126 | 77 | 404 | 83 | 135 | 31 | 27
Estimated technically recoverable shale gas resources | 665 | 802 | 573 | 245 | 545 | 167 | 55 | 36

## Slide 4
North American shale plays

## Slide 5: Americas natural gas production is pulling away from other regions
Chart: 
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Americas | 31.0219 | 30.8668 | 30.638 | 31.8524 | 32.3569 | 33.0981 | 32.9501 | 34.0211 | 35.5275 | 37.1105
Former Soviet Union | 25.7571 | 26.3548 | 26.793 | 27.4633 | 27.752 | 28.0887 | 24.507 | 26.848 | 28.5169 | 28.1246
Middle East | 9.1837 | 9.9458 | 11.262 | 11.9488 | 12.593 | 13.51 | 14.6686 | 15.9369 | 17.7801 | 19.2037
Asia & Oceania | 10.8864 | 11.2546 | 12.118 | 13.0826 | 13.8703 | 14.4703 | 15.371 | 16.939 | 17.1721 | 17.2268
Europe | 11.4771 | 11.9274 | 11.4264 | 11.0989 | 10.7258 | 11.1132 | 10.5604 | 10.8364 | 9.8732 | 9.2814
Africa | 5.1065 | 5.2884 | 6.1559 | 6.5452 | 6.7492 | 7.3893 | 7.1107 | 7.3726 | 7.1235 | 7.4895
dry natural gas production by region
trillion cubic feet
Source: EIA, International Energy Statistics

## Slide 6: Total dry natural gas production in the Americas is outpacing consumption, largely driven by U.S. shale gas production
Source: EIA, International Energy Statistics
United States
Canada
Mexico
Trinidad & Tobago
Argentina
Venezuela
Brazil
Other Americas
Chart: 
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Other Americas | 0.574 | 0.662 | 0.824 | 0.878 | 0.957 | 1.076 | 1.058 | 1.276 | 1.442 | 0.871
Brazil | 0.311 | 0.341 | 0.345 | 0.349 | 0.347 | 0.446 | 0.363 | 0.445 | 0.515 | 0.614
Venezuela | 0.862 | 0.961 | 0.828 | 0.918 | 0.732 | 0.733 | 0.651 | 0.88 | 0.887 | 0.803
Argentina | 1.449 | 1.585 | 1.611 | 1.628 | 1.583 | 1.556 | 1.461 | 1.416 | 1.369 | 1.329
Trinidad and Tobago | 0.874 | 0.992 | 1.069 | 1.287 | 1.378 | 1.388 | 1.437 | 1.499 | 1.434 | 1.448
Mexico | 1.4 | 1.252 | 1.349 | 1.741 | 1.678 | 1.694 | 1.722 | 1.799 | 1.761 | 1.684
Canada | 6.453 | 6.483 | 6.561 | 6.548 | 6.416 | 6.046 | 5.634 | 5.39 | 5.218 | 5.054
United States | 19.099 | 18.591 | 18.051 | 18.504 | 19.266 | 20.159 | 20.624 | 21.316 | 22.902 | 25.308
Chart: 
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Other Americas | 0.65 | 0.669 | 0.727 | 0.732 | 0.684 | 0.691 | 0.745 | 0.906 | 0.907 | 1.819
Brazil | 0.499 | 0.608 | 0.657 | 0.683 | 0.701 | 0.835 | 0.661 | 0.89 | 0.885 | 1.031
Venezuela | 0.862 | 0.961 | 0.828 | 0.918 | 0.736 | 0.786 | 0.714 | 0.957 | 0.961 | 0.869
Argentina | 1.221 | 1.339 | 1.428 | 1.475 | 1.551 | 1.568 | 1.523 | 1.529 | 1.629 | 1.641
Trinidad and Tobago | 0.453 | 0.5 | 0.575 | 0.713 | 0.715 | 0.775 | 0.74 | 0.824 | 0.811 | 0.807
Mexico | 1.64 | 1.653 | 1.656 | 2.2 | 2.025 | 2.129 | 2.135 | 2.286 | 2.364 | 2.424
Canada | 3.373 | 3.341 | 3.404 | 3.307 | 3.115 | 3.011 | 3.063 | 2.913 | 3.164 | 2.936
United States | 22.277 | 22.403 | 22.014 | 21.699 | 23.104 | 23.277 | 22.91 | 24.087 | 24.385 | 25.533

## Slide 7: These seven regions accounted for 95% of U.S. oil production growth and all U.S. natural gas production growth from 2011-2013
Source: EIA, Drilling Productivity Report

## Slide 8: The U.S. has experienced a rapid increase in natural gas and oil production from shale and other tight resources
Chart: 
Chart: 
Sources: EIA derived from state administrative data collected by DrillingInfo Inc. Data are through August 2014 and represent EIA’s official tight oil & shale gas estimates, but are not survey data. State abbreviations indicate primary state(s).

## Slide 9: U.S. shale gas leads growth in total gas production through 2040, when production exceeds 100 billion cubic feet per day
U.S. dry natural gas production
trillion cubic feet
Source: EIA, Annual Energy Outlook 2014, Reference case
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040
Coalbed methane | 0.29543 | 0.3872 | 0.35706 | 0.62802 | 0.67459 | 0.8798 | 1.0852 | 1.177 | 1.312 | 1.389 | 1.508 | 1.604 | 1.6574 | 1.7054 | 1.7233 | 1.7541 | 1.838 | 1.8029 | 1.654 | 1.917 | 1.8083 | 1.7312 | 1.5822 | 1.6372 | 1.5519 | 1.5367 | 1.5541 | 1.6082 | 1.669 | 1.6885 | 1.6641 | 1.6631 | 1.6405 | 1.6347 | 1.6259 | 1.6143 | 1.5935 | 1.5758 | 1.5723 | 1.5887 | 1.611 | 1.6189 | 1.6253 | 1.6318 | 1.6376 | 1.6427 | 1.6743 | 1.6826 | 1.6775 | 1.6908 | 1.7054
Associated with oil | 2.6955 | 2.7202 | 2.7469 | 2.5571 | 2.5745 | 2.5745 | 2.5464 | 2.5858 | 2.7336 | 2.9303 | 2.8397 | 2.7793 | 2.5476 | 2.4429 | 2.2832 | 2.0362 | 1.9608 | 1.9537 | 2.014 | 2.1067 | 2.0621 | 2.1802 | 2.5336 | 2.9248 | 3.1068 | 3.1462 | 3.3819 | 3.3503 | 3.3586 | 3.3542 | 3.3319 | 3.2987 | 3.282 | 3.2372 | 3.1917 | 3.1648 | 3.0982 | 3.0112 | 2.9309 | 2.861 | 2.833 | 2.7862 | 2.7423 | 2.7027 | 2.6768 | 2.652 | 2.6292 | 2.6393 | 2.6236 | 2.6458 | 2.62
Alaska | 0.38143 | 0.40938 | 0.41159 | 0.39809 | 0.52446 | 0.4345 | 0.44238 | 0.42678 | 0.42653 | 0.42456 | 0.41967 | 0.43529 | 0.4286 | 0.45644 | 0.43885 | 0.45933 | 0.42009 | 0.40715 | 0.37411 | 0.37415 | 0.35339 | 0.33467 | 0.32921 | 0.31921 | 0.30535 | 0.29982 | 0.29491 | 0.29051 | 0.28625 | 0.28188 | 0.27736 | 0.27298 | 0.26862 | 0.2643 | 0.25998 | 0.25562 | 0.48916 | 0.72271 | 0.95631 | 1.19 | 1.1858 | 1.1816 | 1.1784 | 1.1765 | 1.1755 | 1.1744 | 1.1733 | 1.1722 | 1.1708 | 1.1691 | 1.1672
Non-associated offshore | 4.6942 | 4.4568 | 4.3519 | 4.4204 | 4.6656 | 4.5629 | 4.7455 | 4.6306 | 4.5173 | 4.2004 | 4.1148 | 4.1819 | 3.7514 | 3.812 | 3.3432 | 2.6864 | 2.4548 | 2.3667 | 2.0628 | 2.0014 | 1.8537 | 1.3506 | 1.1824 | 1.3353 | 1.4688 | 1.4728 | 1.5779 | 1.629 | 1.5861 | 1.5155 | 1.4787 | 1.4559 | 1.4192 | 1.4925 | 1.515 | 1.5279 | 1.5946 | 1.6628 | 1.7162 | 1.7693 | 1.8403 | 1.874 | 1.8968 | 1.8812 | 1.8648 | 1.8721 | 1.9316 | 2.0158 | 2.0578 | 2.1671 | 2.2419
Non-associated onshore | 7.7574 | 7.6375 | 7.6967 | 7.508 | 7.666 | 7.3069 | 7.1284 | 6.9694 | 6.7393 | 6.5337 | 6.6817 | 6.7388 | 6.4533 | 6.3179 | 6.0222 | 5.7802 | 5.8407 | 5.8701 | 6.2087 | 5.0752 | 4.9001 | 4.0044 | 3.8571 | 3.3841 | 3.0608 | 2.9084 | 2.8692 | 2.7969 | 2.7495 | 2.6293 | 2.5324 | 2.5168 | 2.4173 | 2.3641 | 2.312 | 2.2505 | 2.1826 | 2.1319 | 2.0739 | 2.029 | 1.9838 | 1.9272 | 1.8308 | 1.7885 | 1.7444 | 1.7179 | 1.6996 | 1.6627 | 1.6329 | 1.6127 | 1.5756
Tight gas | 1.8137 | 1.8972 | 2.0863 | 2.388 | 2.5078 | 2.6232 | 2.7443 | 2.8557 | 3.0349 | 3.0904 | 3.3211 | 3.535 | 3.6655 | 3.8631 | 4.2022 | 4.6074 | 4.9703 | 5.3426 | 5.866 | 5.7343 | 5.4744 | 5.0051 | 4.8623 | 5.2336 | 5.1599 | 5.3058 | 5.5568 | 5.7941 | 6.091 | 6.3276 | 6.478 | 6.6463 | 6.7598 | 6.8373 | 6.9484 | 7.0594 | 7.1682 | 7.3627 | 7.6527 | 7.8495 | 8.0565 | 8.1998 | 8.3184 | 8.416 | 8.4824 | 8.5336 | 8.3916 | 8.341 | 8.3202 | 8.3406 | 8.4108
Shale gas | 0.17203 | 0.18955 | 0.18954 | 0.19582 | 0.20804 | 0.21678 | 0.16197 | 0.25703 | 0.25999 | 0.26398 | 0.29701 | 0.34194 | 0.42398 | 0.50098 | 0.57796 | 0.72697 | 1.019 | 1.5229 | 1.979 | 3.415 | 4.8634 | 7.9422 | 9.7162 | 9.3512 | 9.6253 | 9.9598 | 10.4463 | 10.9099 | 11.4617 | 12.3941 | 13.3271 | 13.8474 | 14.4011 | 15.0943 | 15.5845 | 15.9923 | 16.3389 | 16.6034 | 16.745 | 16.7994 | 16.9182 | 17.0765 | 17.4484 | 17.7955 | 18.1502 | 18.5004 | 18.8607 | 19.1686 | 19.558 | 19.7341 | 19.8239


Coalbed methane | 0.80939 | 1.0608 | 0.97823 | 1.7206 | 1.8482 | 2.4104 | 2.9731 | 3.2246 | 3.5945 | 3.8054 | 4.1316 | 4.3946 | 4.5408 | 4.6722 | 4.7214 | 4.8057 | 5.0356 | 4.9395 | 4.5315 | 5.2521 | 4.9542 | 4.7429 | 4.3348 | 4.4856 | 4.2518 | 4.2101 | 4.2579 | 4.4061 | 4.5726 | 4.6262 | 4.5591 | 4.5565 | 4.4945 | 4.4785 | 4.4544 | 4.4228 | 4.3657 | 4.3174 | 4.3078 | 4.3526 | 4.4136 | 4.4353 | 4.453 | 4.4708 | 4.4867 | 4.5006 | 4.5871 | 4.6098 | 4.596 | 4.6323 | 4.6723
Associated with oil | 7.3848 | 7.4527 | 7.5256 | 7.0058 | 7.0533 | 7.0535 | 6.9764 | 7.0844 | 7.4892 | 8.0282 | 7.78 | 7.6145 | 6.9798 | 6.6928 | 6.2552 | 5.5786 | 5.372 | 5.3525 | 5.5177 | 5.7719 | 5.6496 | 5.9731 | 6.9414 | 8.0132 | 8.5117 | 8.6198 | 9.2654 | 9.1789 | 9.2018 | 9.1897 | 9.1285 | 9.0376 | 8.9918 | 8.869 | 8.7443 | 8.6707 | 8.4883 | 8.2498 | 8.03 | 7.8384 | 7.7617 | 7.6333 | 7.5132 | 7.4047 | 7.3338 | 7.2658 | 7.2033 | 7.2308 | 7.1878 | 7.2487 | 7.1781
Alaska | 1.045 | 1.1216 | 1.1277 | 1.0907 | 1.4369 | 1.1904 | 1.212 | 1.1692 | 1.1686 | 1.1632 | 1.1498 | 1.1926 | 1.1742 | 1.2505 | 1.2023 | 1.2584 | 1.1509 | 1.1155 | 1.0249 | 1.0251 | 0.96819 | 0.91691 | 0.90194 | 0.87454 | 0.83657 | 0.82141 | 0.80798 | 0.79593 | 0.78424 | 0.77228 | 0.75989 | 0.74789 | 0.73594 | 0.7241 | 0.71226 | 0.70034 | 1.3402 | 1.98 | 2.62 | 3.2602 | 3.2488 | 3.2373 | 3.2284 | 3.2232 | 3.2205 | 3.2175 | 3.2146 | 3.2116 | 3.2077 | 3.203 | 3.1977
Associated with oil
Coalbed methane
Tight gas
Shale gas
Alaska
Non-associated offshore
Non-associated onshore
projections
history
2012
billion cubic feet per day
Notes: 9
9
trillion cubic feet |  |  |  |  |  |  | 2012-2040 | 2012-2040
 | 1990 | 2000 | 2012 | 2015 | 2025 | 2040 | %change | AAGR, %
Coalbed methane | 0.3 | 1.5 | 1.6 | 1.5 | 1.6 | 1.7 | 7.8% | 0.3%
Associated with oil | 2.7 | 2.8 | 2.5 | 3.2 | 3.2 | 2.6 | 3.4% | 0.1%
Alaska | 0.4 | 0.4 | 0.3 | 0.3 | 0.3 | 1.2 | 254.5% | 4.6%
Non-associated offshore | 4.7 | 4.1 | 1.2 | 1.5 | 1.5 | 2.2 | 89.6% | 2.3%
Non-associated onshore | 7.8 | 6.7 | 3.9 | 2.9 | 2.3 | 1.6 | -59.2% | -3.1%
Tight gas | 1.8 | 3.3 | 4.9 | 5.3 | 7.1 | 8.4 | 73.0% | 2.0%
Shale gas | 0.2 | 0.3 | 9.7 | 10.0 | 16.0 | 19.2 | 104.0% | 2.6%
Total | 17.8 | 19.2 | 24.1 | 24.6 | 31.9 | 37.5 | 56.0% | 1.6%

## Slide 10: Natural gas consumption growth is driven by electric power, industrial, and transportation use
Chart: 
| 2005 | 2012 | 2020 | 2025 | 2030 | 2035 | 2040
Residential | 4.8268 | 4.1797 | 4.459 | 4.4038 | 4.3324 | 4.2272 | 4.1156
Commercial | 2.9989 | 2.9069 | 3.1646 | 3.2175 | 3.2812 | 3.4046 | 3.5693
Transportation | 0.60691 | 0.74799 | 0.80582 | 0.88862 | 1.0786 | 1.295 | 1.6781
Gas to Liquids | 0 | 0 | 0 | 0 | 0 | 0 | 0
Industrial | 7.7127 | 8.5309 | 9.823 | 10.3553 | 10.6355 | 10.8363 | 11.0352
Electric Power | 5.8691 | 9.1367 | 8.8081 | 9.486 | 10.0606 | 10.674 | 11.2316
U.S. dry gas consumption
trillion cubic feet
Source: EIA, Annual Energy Outlook 2014, Reference case
projections
history
industrial*
electric
power
commercial
residential
transportation**
11.2
4.1
1.7
11.0
3.6
9.1
4.2
0.7
8.5
2.9
*Includes combined heat-and-power and lease and plant fuel
**Includes pipeline fuel

## Slide 11: U.S. becomes a net exporter of natural gas in the near future
U.S. dry natural gas
trillion cubic feet per year
Source: EIA, Annual Energy Outlook 2014 Reference case
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Net Imports | -1.4467 | -1.6441 | -1.9212 | -2.2099 | -2.4621 | -2.6869 | -2.784 | -2.8372 | -2.9931 | -3.4221 | -3.5379 | -3.6037 | -3.4992 | -3.2638 | -3.4044 | -3.6124 | -3.4623 | -3.7851 | -3.0208 | -2.679 | -2.604 | -1.9616 | -1.519 | -1.3402 | -1.345 | -1.0843 | -0.75553 | -0.030024 | 0.65882 | 1.4031 | 1.9261 | 2.2981 | 2.4864 | 2.8779 | 3.192 | 3.4102 | 3.7354 | 4.1116 | 4.4456 | 4.764 | 4.937 | 5.0411 | 5.2406 | 5.3372 | 5.4127 | 5.5311 | 5.6225 | 5.6846 | 5.7645 | 5.849 | 5.798
Supply | 17.7269 | 17.918 | 18.307 | 18.5799 | 18.785 | 19.52 | 19.8251 | 19.9002 | 19.2529 | 18.9831 | 19.7952 | 18.635 | 19.5278 | 19.0127 | 18.9981 | 18.402 | 18.2367 | 19.3187 | 20.2562 | 20.2311 | 21.4828 | 22.4229 | 23.9833 | 24.3132 | 23.8577 | 24.4211 | 25.5779 | 26.2771 | 27.0988 | 28.088 | 28.9866 | 29.5978 | 30.0852 | 30.8212 | 31.3341 | 31.7614 | 32.3617 | 32.9672 | 33.5442 | 33.9835 | 34.3253 | 34.5606 | 34.9355 | 35.2772 | 35.6133 | 35.9682 | 36.2375 | 36.5598 | 36.9151 | 37.232 | 37.4279
Consumption | 19.1736 | 19.5621 | 20.2282 | 20.7898 | 21.2471 | 22.2069 | 22.6091 | 22.7373 | 22.246 | 22.4052 | 23.3331 | 22.2386 | 23.027 | 22.2765 | 22.4025 | 22.0144 | 21.6991 | 23.1038 | 23.277 | 22.9101 | 24.0868 | 24.3846 | 25.5023 | 25.6534 | 25.2027 | 25.5055 | 26.3334 | 26.3071 | 26.44 | 26.6849 | 27.0605 | 27.2997 | 27.5988 | 27.9433 | 28.1421 | 28.3512 | 28.6263 | 28.8557 | 29.0986 | 29.2195 | 29.3883 | 29.5195 | 29.6948 | 29.94 | 30.2006 | 30.4371 | 30.615 | 30.8752 | 31.1507 | 31.383 | 31.6299
projections
history
2012
Consumption
Domestic supply
Net exports
100
75
50
25
0
-25
billion cubic feet per day
Notes: trillion cubic feet |  |  |  |  |  |  |  | 2012-2040 | 2012-2040
 | 1990 | 2000 | 2008 | 2012 | 2017 | 2025 | 2040 | %change | AAGR, %
Consumption | 19.2 | 23.3 | 23.3 | 25.5 | 26.3 | 28.4 | 31.6 | 24.0% | 0.8%
Supply | 17.7 | 19.8 | 20.3 | 24.0 | 26.3 | 31.8 | 37.4 | 56.1% | 1.6%
Net Exports | -1.5 | -3.5 | -3.0 | -1.6 | 0.0 | 3.4 | 5.8 | 481.7% | NA

## Slide 12: Projected U.S. natural gas trade depends on assumptions regarding resources and future technology advances
Source: EIA, Annual Energy Outlook 2014, Reference case and High Oil and Gas Resource case
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Alaska LNG exports | 0.0301 | 0.016398 | 0.009342 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lower 48 states LNG exports | 0 | 0 | 0 | 0 | 0 | 0.1 | 0.3 | 0.75 | 1.25 | 1.76 | 2.47 | 2.87 | 3.11 | 3.51 | 4.11 | 4.71
Exports to Canada | 0.73874 | 0.93699 | 0.97085 | 0.99377 | 1.0288 | 0.99337 | 0.94317 | 0.93692 | 0.94487 | 0.95503 | 0.9563 | 0.92541 | 0.9258 | 0.95409 | 0.98412 | 1.052
Exports to Mexico | 0.33346 | 0.5003 | 0.61996 | 0.71374 | 0.75174 | 0.92452 | 1.0539 | 1.0747 | 1.1058 | 1.1624 | 1.2043 | 1.2719 | 1.3457 | 1.4386 | 1.5282 | 1.6642
Imports from Canada | -3.2798 | -3.1171 | -2.9587 | -3.0272 | -3.1153 | -3.1301 | -3.0522 | -2.8091 | -2.6137 | -2.4507 | -2.3136 | -2.2 | -2.0986 | -2.048 | -2.0309 | -2.0191
Imports from Mexico | -0.029995 | -0.002672 | -0.000314 | -0.0003 | -0.0003 | -0.0003 | -0.049105 | -0.003025 | -0.0003 | -0.0003 | -0.0003 | -0.0003 | -0.0003 | -0.0003 | -0.0003 | -0.0003
LNG Imports | -0.43101 | -0.34894 | -0.17465 | -0.13141 | -0.1459 | -0.14695 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Alaska LNG exports | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Lower 48 states LNG exports | 0.064585 | 0.069765 | 0.028143 | 0.008 | 0.008 | 0.108 | 0.308 | 0.758 | 1.258 | 1.768 | 2.078 | 2.318 | 2.318 | 2.518 | 2.718 | 2.718
Exports to Canada | 0.73874 | 0.93699 | 0.97085 | 0.99377 | 1.0288 | 1.0143 | 0.99201 | 1.0229 | 1.0446 | 1.0591 | 1.081 | 1.0779 | 1.107 | 1.1326 | 1.1437 | 1.183
Exports to Mexico | 0.33346 | 0.5003 | 0.61996 | 0.71374 | 0.75174 | 0.90138 | 1.0196 | 1.0244 | 1.0358 | 1.0736 | 1.1026 | 1.1554 | 1.2156 | 1.2972 | 1.3738 | 1.4977
Imports from Canada | -3.2798 | -3.1171 | -2.9587 | -2.924 | -2.9873 | -2.9583 | -2.8747 | -2.6819 | -2.5313 | -2.3493 | -2.1871 | -2.1049 | -2.0059 | -1.9217 | -1.8952 | -1.8403
Imports from Mexico | -0.029995 | -0.002672 | -0.000314 | -0.0003 | -0.0003 | -0.002816 | -0.052376 | -0.005357 | -0.0003 | -0.0003 | -0.0003 | -0.0003 | -0.0003 | -0.0003 | -0.0003 | -0.0003
LNG Imports | -0.43101 | -0.34894 | -0.17465 | -0.13141 | -0.1459 | -0.14695 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148 | -0.148
Reference case
trillion cubic feet per year
exports to Mexico
exports to Canada
lower 48
LNG exports
imports from Canada
LNG imports
High Oil and Gas Resource case
trillion cubic feet per year
billion cubic
feet per day
0
5
20
15
10
-5
-10

## Slide 13: Currently, most of the US exports are via pipeline, but liquefied natural gas export projects have been proposed. Proposed non-FTA LNG export facilities as of March 2014 Potential export-oriented natural gas liquefaction facilities
Canada
Mexico
Kitimat: 0.7 Bcf/d proposed
Corpus Christi: 2.1 Bcf/d
Gulf Coast: 2.8 Bcf/d
Jordon Cove: 1.2 Bcf/d
Cove Point:
1.0 Bcf/d
Gulf LNG Liquefaction Company:1.5 Bcf/d
Oregon LNG: 1.25 Bcf/d
Alaska
Kenai: 0.3 Bcf/d
LNG Facilities
Approved for exports
Proposed
Operating
Canadian Facilities
LNG Facility Capacity (Bcf/d)
2 to 3
1 to 2
0 to 1
Source: U.S. Energy Information Administration based on information from the Department of Energy (DOE), Office of Fossil Energy and the Canada’s National
Energy Board. Note: Capacity estimated from larger of FTA or non FTA capacity proposals.
Elba Island: 0.5 Bcf/d
Lavaca Bay, TX: 1.38 Bcf/d
Ingleside, TX: 1.09Bcf/d
CE FLNG: 1.07Bcf/d
Main Pass Energy Hub:3.2 Bcf/d
Douglas Island: 0.25 Bcf/d
Prince Rupert Island: 1.0 Bcf/d
Kitimat: 2.0 Bcf/d potential
Goldboro: 0.67 Bcf/d potential
Melford: 1.8 Bcf/d potential
EOS FLNG: 1.6 Bcf/d
Barca FLNG:
1.6 Bcf/d
Texas
Louisiana
Lake
Charles
2.0 Bcf/d
Sabine Pass:
2.2 Bcf/d approved
0.9 Bcf/d proposed
Golden Pass:
2.6 Bcf/d
Cameron: 1.7 Bcf/d
Venture Global: 0.7 Bcf/d
Freeport:
2.8 Bcf/d approved
Delfin
1.8 Bcf/d
Magnolia
1.08 Bcf/d

## Slide 14: Most liquefaction projects are in North America and will increase the region’s total capacity 8-fold by 2019
Liquefaction (bcf/d) |  |  | 
Country | Operating | Construction | Engineering
Peru | 0.6 |  | 
Trinidad and Tobago | 2.0 |  | 
Colombia |  | 0.1 | 
United States |  | 1.2 | 13.1
Brazil |  |  | 0.4
Canada |  |  | 3.3
Total | 2.6 | 1.3 | 16.8
Regasification (bcf/d) |  |  | 
Country | Operating | Construction | Engineering
Argentina | 0.9 |  | 
Brazil | 1.2 | 0.8 | 
Canada | 1.0 |  | 
Chile | 0.6 |  | 
Dominican Republic | 0.2 |  | 
Mexico | 2.3 |  | 
Puerto Rico | 0.4 |  | 
United States | 10.2 |  | 
Total | 16.8 | 0.8 | 0
Source: IHS EDIN
Note: Displays larger import/export facilities only
Liquefaction, operating
Liquefaction, construction
Liquefaction, engineering
Regasification, operating
Regasification, construction

## Slide 15: Currently, the Panama Canal can accommodate only 9% of the world’s LNG carrier fleet; after the expansion, it will be able to accommodate 88% of currently active carriers
The Panama Canal and the Trans-Panama Pipeline are not currently used for significant volumes of petroleum trade and no LNG trade
The Panama Canal expansion project will open the canal route to Aframax tankers and 80% of the current global LNG carrier fleet, resulting in increased regional petroleum and LNG trade
By 2019, liquefaction capacity in the Americas is expected to increase eight-fold, with most of the projects in the United States
EIA anticipates increased LNG trade between countries in the Americas, but traffic from the Americas to Asia (the largest LNG import market) through the Panama Canal will also increase

## Slide 16: Shale gas in eastern Canada
Source: Advanced Resources International, “Technically Recoverable Shale Oil and Shale Gas Resources: An Assessment of 137 Shale Formations in 41 Countries Outside the United States”
Of the four shale plays in Eastern Canada, two have been assessed by ARI
  Utica in Quebec has 31.1 Tcf of technically recoverable resources
  Horton Bluff in Nova Scotia has 3.4 Tcf of technically recoverable resources
These shale resource volumes are not included in NEB’s 2013 estimates
Quebec enacted a hydraulic fracturing moratorium in 2012 pending further research
New Brunswick permits hydraulic fracturing, but has imposed strict rules surrounding it
Nova Scotia, similar to Quebec, will not permit hydraulic fracturing until the completion of a review, due mid-2014

## Slide 17: LNG export projects in eastern Canada
Source: Company websites
 | Goldboro LNG Terminal | H-Energy LNG Terminal
Planned year in service | 2019 | 2020
Liquefaction capacity | 1.3 Bcf/d | 0.6 Bcf/d
Storage capacity | 14.6 Bcf | N/A
Contract | 20 year supply deal with E. On AG | N/A
Supply sources | Marcellus, eastern Canada | N/A
NEB approval | Under review | N/A
Maine

## Slide 18: Resources in eastern Canada are modest compared with the Canada national total
Note: WCSB stands for Western Canada Sedimentary Basin . All Territories are included under Northern Canada.
Source: National Energy Board, “Canada’s Energy Future 2013”
Canada marketable resources in trillion cubic feet
as of 12/31/12
Chart: 
| WCSB* | Northern Canada | East coast | West coast | Ontario and Quebec
 | 861 | 116 | 91 | 17 | 8
BC
AB
YK
NT
SK
MB
ON
QC
NS
NB
NL
NU

## Slide 19: Key Takeaways from Updated EIA Study of added LNG exports
Prices: Projected average natural gas prices at the producer level average 4% to 11% above the Reference case projection across export scenarios over 2015-40, while residential natural gas prices in the export scenarios average 2% to 5% above their base projection
Natural gas production: With the exception of one baseline/scenario pairing, higher natural gas production satisfies 60% to 80% of the increase in natural gas demand from LNG exports over 2015-40
Natural gas consumption: The electric power sector accounts for most of the decrease in delivered natural gas. The electric generation mix shifts towards other generation sources, including coal and renewables, with some decrease in total generation as electricity prices rise
CO2 emissions: Higher coal use leads to higher carbon dioxide output
Expenditures: On average, from 2015 to 2040, natural gas bills paid by end-use consumers in the residential, commercial and industrial sectors combined increase 1% to 8% across pairings of export scenarios and baselines. Increases in electricity bills paid by end-use customers range from 0% to 3%
Economic gains: Changes in the level of GDP relative to baseline range from 0.05% to 0.17% and generally increase with the amount of added LNG exports required to fulfill an export scenario; EIA’s NEMS model may understate the economic benefits

## Slide 20: Areas of uncertainty in the outlook
Oil and natural gas prices
China’s energy demand growth; particularly in transportation
Increasing global trade of natural gas and hydrocarbon gas liquids in addition to oil
Global development of tight oil and shale gas resources
Policy decisions on crude oil exports and pipeline permits
Impact of geopolitical tensions on energy supply
Constraints on CO2

## Slide 21: For more information
U.S. Energy Information Administration home page | www.eia.gov
Annual Energy Outlook | www.eia.gov/aeo
Short-Term Energy Outlook | www.eia.gov/steo
International Energy Outlook | www.eia.gov/ieo
Monthly Energy Review | www.eia.gov/mer
Today in Energy | www.eia.gov/todayinenergy
State Energy Portal | www.eia.gov/state
Drilling Productivity Report | www.eia.gov/petroleum/drilling/

## Slide 22
Supplemental Slides

## Slide 23: A larger share of new wells produce both oil and natural gas
marketed gas production
non-marketed gas production
Chart: 
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 YTD
oil & gas | 19080 | 22913 | 14654 | 19486 | 22519 | 25244 | 23635 | 10385
oil only | 6734 | 8483 | 5484 | 6872 | 10353 | 9338 | 9117 | 3672
gas only | 25828 | 26388 | 15601 | 14170 | 11694 | 8653 | 6307 | 2295
natural gas only
oil only
oil and natural gas
Note: 2014 figure represents averages from January to September 2014
Source: EIA based on DrillingInfo

## Slide 24: Resource and technology assumptions have major implications for projected U.S. crude oil production beyond the next few years
Chart: 
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025
Alaska | 1.774 | 1.798 | 1.7143 | 1.584 | 1.559 | 1.481 | 1.3922 | 1.296 | 1.175 | 1.0503 | 0.97034 | 0.963 | 0.985 | 0.975 | 0.90851 | 0.864 | 0.741 | 0.722 | 0.685 | 0.646 | 0.599 | 0.572 | 0.53 | 0.51 | 0.4738 | 0.46283 | 0.46216 | 0.46994 | 0.47196 | 0.454 | 0.43714 | 0.41284 | 0.38871 | 0.36631 | 0.34569 | 0.32667
Offshore | 0.954 | 1.023 | 1.0691 | 1.09 | 1.138 | 1.261 | 1.3144 | 1.401 | 1.473 | 1.558 | 1.6126 | 1.705 | 1.715 | 1.717 | 1.5986 | 1.421 | 1.434 | 1.406 | 1.274 | 1.674 | 1.669 | 1.425 | 1.365 | 1.37 | 1.49 | 1.6312 | 2.0072 | 1.9699 | 1.9616 | 1.9756 | 1.9033 | 1.7924 | 1.7115 | 1.6742 | 1.6193 | 1.6372
Other onshore | 4.626 | 4.588 | 4.383 | 4.17 | 3.96 | 3.812 | 3.7547 | 3.752 | 3.602 | 3.272 | 3.0851 | 2.983 | 2.903 | 2.843 | 2.752 | 2.707 | 2.727 | 2.71 | 2.397 | 2.36 | 2.338 | 2.347 | 2.345 | 2.3665 | 2.4914 | 2.4493 | 2.4047 | 2.3987 | 2.3843 | 2.3978 | 2.4234 | 2.4101 | 2.4439 | 2.4735 | 2.4959 | 2.4986
Tight oil | 0.004 | 0.007 | 0.006 | 0.005 | 0.004 | 0.003 | 0.002 | 0.002 | 0.002 | 0.001 | 0.154 | 0.151 | 0.142 | 0.146 | 0.159 | 0.185 | 0.2 | 0.227 | 0.608 | 0.687 | 0.868 | 1.314 | 2.254 | 3.4755 | 4.0736 | 4.4944 | 4.6677 | 4.7183 | 4.7576 | 4.7808 | 4.7887 | 4.8012 | 4.7447 | 4.6768 | 4.612 | 4.5418
STEO | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | 6.5 | 7.44 | 8.54 | 9.5 | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Alaska | 1.774 | 1.798 | 1.7143 | 1.584 | 1.559 | 1.481 | 1.3922 | 1.296 | 1.175 | 1.0503 | 0.97034 | 0.963 | 0.985 | 0.975 | 0.90851 | 0.864 | 0.741 | 0.722 | 0.685 | 0.646 | 0.599 | 0.572 | 0.53 | 0.51 | 0.4738 | 0.46283 | 0.46216 | 0.46994 | 0.47196 | 0.47516 | 0.48653 | 0.48339 | 0.49736 | 0.52575 | 0.53475 | 0.56755
Offshore | 0.954 | 1.023 | 1.0691 | 1.09 | 1.138 | 1.261 | 1.3144 | 1.401 | 1.473 | 1.558 | 1.6126 | 1.705 | 1.715 | 1.717 | 1.5986 | 1.421 | 1.434 | 1.406 | 1.274 | 1.674 | 1.669 | 1.425 | 1.365 | 1.37 | 1.49 | 1.8223 | 2.0876 | 2.1139 | 2.1262 | 2.135 | 2.1079 | 2.0036 | 1.9338 | 1.8244 | 1.8025 | 1.7839
Other onshore | 4.626 | 4.588 | 4.383 | 4.17 | 3.96 | 3.812 | 3.7547 | 3.752 | 3.602 | 3.272 | 3.0851 | 2.983 | 2.903 | 2.843 | 2.752 | 2.707 | 2.727 | 2.71 | 2.397 | 2.36 | 2.338 | 2.347 | 2.345 | 2.3614 | 2.4606 | 2.4303 | 2.3307 | 2.3379 | 2.314 | 2.3184 | 2.3262 | 2.3316 | 2.3816 | 2.4553 | 2.5185 | 2.4928
Tight oil | 0.004 | 0.007 | 0.006 | 0.005 | 0.004 | 0.003 | 0.002 | 0.002 | 0.002 | 0.001 | 0.154 | 0.151 | 0.142 | 0.146 | 0.159 | 0.185 | 0.2 | 0.227 | 0.608 | 0.687 | 0.868 | 1.314 | 2.254 | 3.6328 | 4.4976 | 5.1261 | 5.4291 | 5.8757 | 6.1861 | 6.3728 | 6.4924 | 6.8481 | 7.1626 | 7.3142 | 7.4919 | 7.6649
STEO | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | 6.5 | 7.44 | 8.54 | 9.5 | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A
Source: EIA, Annual Energy Outlook 2014; Short Term Energy Outlook, October 2014
Alaska
tight oil
other lower 48 states onshore
lower 48 states offshore
STEO October 2014 U.S. crude oil projection
2012
projections
history
projections
history
2012
Alaska
tight oil
other lower 48 states onshore
Reference case
million barrels per day
High Oil and Gas Resource case
million barrels per day
lower 48 states offshore

## Slide 25: Most significant contributors to non-OPEC crude and lease condensate production: Canada, Brazil, U.S., Kazakhstan, Russia
Chart: 
| Canada | United States | Mexico | Brazil | Kazakhstan | Russia | Other
2010 | 2.9001 | 5.639 | 2.6408 | 2.0547 | 1.5513 | 9.6856 | 18.395
2025 | 4.9297 | 9.3052 | 2.8048 | 3.1659 | 2.7098 | 10.1107 | 16.3583
2040 | 5.9176 | 7.7931 | 3.4146 | 4.5023 | 3.1018 | 11.0992 | 17.0302
non-OPEC crude and lease condensate production, Reference case
million barrels per day
Source: EIA, International Energy Outlook 2014

## Slide 26: In the Americas, recent gains in oil production are concentrated in countries with open investment structures
crude oil production by select Americas country
million barrels per day
Source: EIA, International Energy Statistics
Chart: 
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
United States | 5.6441 | 5.4351 | 5.1857 | 5.0886 | 5.0769 | 5.0004 | 5.3529 | 5.4787 | 5.6519 | 6.4864
Canada | 2.3057 | 2.3984 | 2.3689 | 2.5254 | 2.6281 | 2.5793 | 2.5795 | 2.7408 | 2.9006 | 3.1378
Mexico | 3.4587 | 3.4758 | 3.4231 | 3.3454 | 3.143 | 2.839 | 2.6458 | 2.6211 | 2.5998 | 2.5925
Venezuela | 2.3352 | 2.5569 | 2.5647 | 2.5105 | 2.4903 | 2.464 | 2.3195 | 2.2158 | 2.3 | 2.3
Brazil | 1.4961 | 1.4774 | 1.6336 | 1.7227 | 1.748 | 1.8122 | 1.9504 | 2.0547 | 2.1054 | 2.0612
Colombia | 0.54073 | 0.52876 | 0.52579 | 0.53104 | 0.53114 | 0.58836 | 0.67065 | 0.78553 | 0.91425 | 0.94422
Argentina | 0.78311 | 0.73266 | 0.70365 | 0.69645 | 0.67878 | 0.66122 | 0.65118 | 0.62606 | 0.58143 | 0.55112
Ecuador | 0.41101 | 0.52824 | 0.53198 | 0.53568 | 0.51109 | 0.50473 | 0.48562 | 0.48609 | 0.49951 | 0.50359

## Slide 27: Tight oil production will spread to nations outside of the United States and Canada over the projection
Chart: 
| United States | Canada | Mexico | Russia | Argentina | China | Rest of world
2010 | 0.868 | 0.11764 | 0 | 0 | 0 | 0 | 0
2025 | 4.5418 | 0.86828 | 0.23603 | 0.625 | 0.67456 | 0.24148 | 0.35791
2040 | 3.1965 | 1.2501 | 0.32857 | 2.1563 | 0.82141 | 0.16923 | 1.1278
tight oil production, Reference case
million barrels per day
Source: EIA, International Energy Outlook 2014
2.9 MMbbl/d in 2013
3.9 MMbbl/d in 2014 (STEO)
AEO2014 High Resource case
5.0 MMbbl/d in 2015 (STEO)